## Slide 1
PAUSE DETECTION & MFCC FEATURE EXTRACTION

## Slide 2: Speech Signal
Slowly time varying signal
5-100 msec  Characteristics are fairly stationary
First 200 msec of Corresponds to
Speech Recording  Silence

## Slide 3: Approach
Probability Density Function  Mahalanobis Distance
(Linear Pattern Classifier)

## Slide 4: Approach
PDF To specify the probability of the random variable falling within a particular range of values
Mahalanobis Distance/Z score  |x-Mean|
Standard Deviation

## Slide 6
OUTPUT
Voice 1 --> 0.9-1.48 sec
Voice 2 --> 2.3-2.6 sec
Voice 3 --> 3.5-3.9 sec
Voice 4 --> 4.6-4.9 sec

## Slide 7
MFCC Feature Extraction

## Slide 8
FFT
Speech Signal
Mel Scale Filtering
Log()
Discrete Cosine Function
Derivative
Spectrum
Mel Frequency Spectrum
Cepstral Coefficients
Feature Vector

## Slide 9: Important Terms
Sampling rate= 16000 Hz
Window size = 32ms
Frame length= Sampling rate * Window size
Number of samples = Sampling rate*Audio duration
Total Number of frames = Number of samples / Frame length
Number of MFCC coefficients per frame = 13
Total number of MFCC coefficients = 13 * Total Number of frames

## Slide 10: Example
Frame length= 16000 * 0.032 = 512
Number of samples for 6secs video = 16000*6 = 96000 samples
Total Number of frames = 96000/512 = 188
Total number of MFCC coefficients = 13*188 = 2444